## Slide 1
Projet COMMUCAN
Relaxometric study of manganese complexes based on a pyclen structure as MRI contrast agents
Marie Devreux1,2, Céline Henoumont1, Fabienne Dioury3, Sébastien Boutry 4, Olivier Vacher3, Luce Vander Elst1, Marc Port3, Robert N. Muller1,4, Olivier Sandre2 and Sophie Laurent1,4.
1University of Mons, General, Organic and Biomedical Chemistry, NMR and Molecular Imaging Laboratory, 7000 Mons, Belgium
2University of Bordeaux, CNRS, Bordeaux INP, ENSCBP, Laboratory of Organic Polymer Chemistry (LCPO), 33607 Pessac, France
3Conservatoire national des arts et métiers (CNAM), GBCM Laboratory, EA 7528, 2 rue Conté, 75003 Paris, HESAM Université, France
4Center for microscopy and molecular imaging (CMMI), ﻿8 rue Adrienne Bolland, 6041 Charleroi, Belgium
COST – 16th March 2021

## Slide 2
1Beam, A. S, et al, Radiol. Technol. 88, 583–589 (2017)
2Gianolio, E., et la, Eur. J. Inorg. Chem. 2019, 137–151 (2019)
Introduction
Gadolinium complexes
Gd-DTPA
Gd-DOTA
Nephrogenic systemic fibrosis (NSF)1
Retention in the brain2
Introduction Results Conclusion & perspectives

## Slide 3
Introduction Results Conclusion & perspectives
Introduction
Gadolinium complexes
Gd-DTPA
Gd-DOTA
Nephrogenic systemic fibrosis (NSF)1
Retention in the brain2
Alternative ?
Manganese complexes
1Beam, A. S, et al, Radiol. Technol. 88, 583–589 (2017)
2Gianolio, E., et la, Eur. J. Inorg. Chem. 2019, 137–151 (2019)

## Slide 4
Introduction Results Conclusion & perspectives
Introduction
Purpose of the work
Pyclen structure
Can be tuned to have one water molecule in the innersphere
7 coordination bond
Increase the kinetic inertness
Increase the thermodynamic stability
Can play on the rotationals correlations time to increase the relaxivity

## Slide 5
Synthesis of the pyclen derivative
Steps :
  Functionalization of the upper and lower part
  Macrocyclization
  Selective deprotection
  Complexation
Introduction Results Conclusion & perspectives

## Slide 6
Synthesis of the pyclen derivative
Functionalization of the upper and lower part
Introduction Results Conclusion & perspectives

## Slide 7
Synthesis of the pyclen derivative
Macrocyclisation step
Introduction Results Conclusion & perspectives

## Slide 8
Synthesis of the pyclen derivative
Selective deprotection steps
R1 = H (commercial product)
R2 = -OCH2CO2Et
R3 = -OCH2CO2-
R4 = -OCH2CONHCH2CCH
R5 = -OCH2CONHCH2CH2NH3+
Introduction Results Conclusion & perspectives

## Slide 9
Synthesis of the pyclen derivative
Introduction Results Conclusion & perspectives

## Slide 10
Relaxometric characterization
Determination of q
First technique by E. Gale et al.1 : the 17O water transverse relaxivity versus inverse of temperature, at 11.75 T
 | r02max (s-1·mM-1) (67.8 MHz) | q (Eq. 1)
MnL1H | 419.2 | 0.82 ± 0.2
MnL2COO- | 458.4 | 0.90 ± 0.2
MnL3CH | 473.4 | 0.93 ± 0.2
MnL4NH3+ | 478.6 | 0.94 ± 0.2
Introduction Results Conclusion & perspectives
1 Gale, E. M., et al, J. Am. Chem. Soc. 2013, 135, 18600−18608.

## Slide 11
Relaxometric characterization
Determination of q
Second technique by J. Peters and C. Geraldes1 : NMRD profiles at 25°C
 |  |  | r1p (s-1·mM-1) (25°C and 0.02 MHz) | q (Eq. 2)
MnL1H |  |  | 7.7 | 1.25 ± 0.4
MnL2COO- |  |  | 8.3 | 1.30 ± 0.4
MnL3CH |  |  | 9.4 | 1.35 ± 0.4
MnL4NH3+ |  |  | 10.0 | 1.42 ± 0.4
Introduction Results Conclusion & perspectives
1 Peters, J. A.; Geraldes, C. F. G. C., Inorganics, 2018, 6, 116.

## Slide 12
Relaxometric characterization
Determination of q
Comparison of the two techniques : 1 water molecule in the innersphere
 | r02max (s-1·mM-1) (67.8 MHz) | q (Eq. 1) | r1p (s-1·mM-1) (25°C and 0.02 MHz) | q (Eq. 2)
MnL1H | 419.2 | 0.82 ± 0.2 | 7.7 | 1.25 ± 0.4
MnL2COO- | 458.4 | 0.90 ± 0.2 | 8.3 | 1.30 ± 0.4
MnL3CH | 473.4 | 0.93 ± 0.2 | 9.4 | 1.35 ± 0.4
MnL4NH3+ | 478.6 | 0.94 ± 0.2 | 10.0 | 1.42 ± 0.4
Introduction Results Conclusion & perspectives

## Slide 13
Relaxometric characterization
Determination of
Measurement of the 17O water transverse relaxation rate as a function of the inverse of temperature, at 11.75 T1
 | (ns)
MnL1H | 6.5 ± 0.4
MnL2COO- | 6.1 ± 0.7
MnL3CH | 8.4 ± 0.9
MnL4NH3+ | 6.35 ± 0.7
MnL1H | 6.5 ± 0.4
MnL2COO- | 6.1 ± 0.7
MnL3CH | 8.4 ± 0.9
MnL4NH3+ | 6.35 ± 0.7
Fast exchange between the water molecule in the innersphere and the water molecules of the bulk
Introduction Results Conclusion & perspectives
1 Swift, T. J.; Connick, R. E., J. Chem. Phys., 1962, 37, 307.

## Slide 14
Relaxometric characterization
NMRD profiles at 37°C
the theoretical fitting of 1H NMRD profiles at 37°C with Bloembergen and Solomon’s theory using the MINUIT minimization software.1,2,3
 | (ps) | (ps) | (ps)
MnL1H | 48.7 ± 3.8 | 119 ± 19.2 | 7.7
MnL2COO- | 57 ± 5.2 | 155 ± 29.5 | 8.3
MnL3CH | 65.6 ± 0.85 | 224 ± 31.6 | 9.4
MnL4NH3+ | 59 ± 0.6 | 272 ± 6760.0 | 10.0
MnL1H | 48.7 ± 3.8 | 119 ± 19.2 | 7.7
MnL2COO- | 57 ± 5.2 | 155 ± 29.5 | 8.3
MnL3CH | 65.6 ± 0.85 | 224 ± 31.6 | 9.4
MnL4NH3+ | 59 ± 0.6 | 272 ± 6760.0 | 10.0
Increase with the presence of the arm on the pyridine
Introduction Results Conclusion & perspectives
1Solomon, I., Phys. Rev., 1955, 99, 559−565.
2Bloembergen, N., J. Chem. Phys., 1957, 27, 572−573.
3Bloembergen, N.; Morgan, L. O., J. Chem. Phys., 1961, 34, 842.
Notes: NMRD profiles were performed for the four pyclen-based manganese complexes in order to evaluate the efficacy of each complex according to the magnetic field or frequency used. The fitting of these profiles according to the theory of Solomon and Bloembergen allows extracting important parameters to understand this efficacy such as the rotational correlation time (𝜏_R) , the electronic relaxation time at zero field (𝜏_SO) and the correlation time that modulates electronic relaxation (𝜏_V). We can see an increase for the Tr when there is the presence of an arm on the pyrdine. The ligand one has a r1 NMR dispersion profile below the other curves, especially at low field.

## Slide 15
Relaxometric characterization
NMRD profiles at 37°C
the theoretical fitting of 1H NMRD profiles at 37°C with Bloembergen and Salomon’s theory using the MINUIT minimization software.1,2,3
 | (ps) | (ps) | (ps)
MnL1H | 48.7 ± 3.8 | 119 ± 19.2 | 7.7
MnL2COO- | 57 ± 5.2 | 155 ± 29.5 | 8.3
MnL3CH | 65.6 ± 0.85 | 224 ± 31.6 | 9.4
MnL4NH3+ | 59 ± 0.6 | 272 ± 6760.0 | 10.0
MnL1H | 48.7 ± 3.8 | 119 ± 19.2 | 7.7
MnL2COO- | 57 ± 5.2 | 155 ± 29.5 | 8.3
MnL3CH | 65.6 ± 0.85 | 224 ± 31.6 | 9.4
MnL4NH3+ | 59 ± 0.6 | 272 ± 6760.0 | 10.0
Slightly lower values for MnL1H and MnL2COO-
Introduction Results Conclusion & perspectives
1Solomon, I., Phys. Rev., 1955, 99, 559−565.
2Bloembergen, N., J. Chem. Phys., 1957, 27, 572−573.
3Bloembergen, N.; Morgan, L. O., J. Chem. Phys., 1961, 34, 842.
Notes: This difference can be ascribed to the electronic properties of the complex which are slightly less favorable than for the other ones: 𝜏_SO is indeed lower compared to the values of the three other complexes.

## Slide 16
Relaxometric characterization
NMRD profiles at 37°C
the theoretical fitting of 1H NMRD profiles at 37°C with Bloembergen and Solomon’s theory using the MINUIT minimization software.1,2,3
 | (ps) | (ps) | (ps)
MnL1H | 48.7 ± 3.8 | 119 ± 19.2 | 7.7
MnL2COO- | 57 ± 5.2 | 155 ± 29.5 | 8.3
MnL3CH | 65.6 ± 0.85 | 224 ± 31.6 | 9.4
MnL4NH3+ | 59 ± 0.6 | 272 ± 6760.0 | 10.0
MnL1H | 48.7 ± 3.8 | 119 ± 19.2 | 7.7
MnL2COO- | 57 ± 5.2 | 155 ± 29.5 | 8.3
MnL3CH | 65.6 ± 0.85 | 224 ± 31.6 | 9.4
MnL4NH3+ | 59 ± 0.6 | 272 ± 6760.0 | 10.0
 | r1 at 20MHz (s-1·mmol-1·L)* | r1 at 60MHz (s-1·mmol-1·L)*
MnL1H | 2.6 | 2.4
MnL2COO- | 2.7 | 2.6
MnL3CH | 3.2 | 3.3
MnL4NH3+ | 2.9 | 2.4
37°C in water*
Introduction Results Conclusion & perspectives
1Solomon, I., Phys. Rev., 1955, 99, 559−565.
2Bloembergen, N., J. Chem. Phys., 1957, 27, 572−573.
3Bloembergen, N.; Morgan, L. O., J. Chem. Phys., 1961, 34, 842.

## Slide 17
Transmetallation evaluation
Evolution of the normalized paramagnetic longitudinal relaxation rate in order to evaluate the transmetallation kinetic between manganese and zinc ions
Experiment performed during 5 days in phosphate buffer at 20 MHz and 37°C. The concentration of Mn-complexes and of competing Zn(II) salt is 2.5 mM, which is much higher than its normal physiological level (10 µM). 1,2
t1/2 half-life of approximately 1350 min
Introduction Results Conclusion & perspectives
1 Laurent, S. et al, Contrast Media Mol., Imaging 2010, 5, 305−308.
2 Laurent, S. et al, Invest. Radiol., 2001, 36, 115−122.

## Slide 18
Phamtom images
Mn2+-complexes at a concentration of 0.5 mM compared with a commercial Gd-complex, Gd-DOTA, at the same concentration, and with pure water
r1 (s-1·mM-1) 9.4T, 37°C | 2.8 ± 0.1 | 2.7 ± 0.1 | 3.1 ± 0.1 | 2.95 ± 0.1 |  | 3.2 ± 0.1
Introduction Results Conclusion & perspectives

## Slide 19
Manganese complexes based on pyclen derivatives
Functionalization of the arm on the pyridin
Close to the Gd-DOTA efficacy
Introduction Results Conclusion & perspectives
Conclusions
Perspectives
Increase of the relaxivity
Thermodynamic stability

## Slide 20
Thank you for your attention
Projet COMMUCAN
Prof. Laurent Sophie
Dr Henoumont Céline
Dr Stanicki Dimitri
Prof Vander Elst Luce
Prof Muller Robert N.
Dr Boutry Sébastien
RMN group
Dr Dioury Fabienne
Prof. Port Marc
Vachez Olivier
Dr Sandre Olivier
Dr Couillaud Franck
Team 3
doi/10.1021/acs.inorgchem.0c03120