## Slide 1
CO2 emissions
Chart: 
| Energy industries | Transport | Manufacturing Industries and Construction | Residential | Industrial Processes and Product Use | Commercial | Agriculture | Other
Other Fuel Combustion Land-Use Change and Forestry Industrial Processes Building Manufacturing/Construction Transportation Electricity/Heat | 2.3413 | 3.1422 | 4.6231 | 7.5962 | 17.2809 | 20.7979 | 44.2184
Electricity and heat
Transport
Manufacturing and construction
Buildings
Industrial processes
Land use change and forestry
Other
CO2 capture
Absorption
Adsorption
Membrane technology
Micro-algae
Cryogenics
CO2 Utilisation or Storage
etc…
Food processing
Chemicals
Fuel and biofuel
High regeneration energy ()
Tempregen around 120 – 130 °C
Reduction of energy consumption by:
Drawback of the process
Context of the study
Conventional amine-based absorption-regeneration process
Innovative solvents
Process optimization
Use of catalysts
Geological storage
Catalyst
Total worldwide CO2 emissions (1990 – 2021) [1]
CO2 emissions by sector in the world (2021) [1]
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
 | 23.0604 | 23.2174 | 23.168 | 23.3112 | 23.4576 | 24.0864 | 24.4347 | 25.5468 | 25.1547 | 25.2276 | 25.9239 | 26.0108 | 26.7312 | 27.6025 | 29.073 | 29.9082 | 31.1394 | 31.8259 | 32.0313 | 31.9533 | 33.522 | 33.4296 | 33.8162 | 34.4695 | 34.8564 | 34.6863 | 35.3833 | 35.8777 | 36.8653 | 37.0463 | 34.8196 | 36.6934
36.7 Gt in 2021
Polymers
etc…
Selection of catalysts for the regeneration step in an amine-based absorption-regeneration CO2 capture process
Célia PASTE (celia.paste@umons.ac.be), Lionel DUBOIS and Diane THOMAS Chemical and Biochemical Process Engineering Unit, Faculty of Engineering, University of Mons, 20 Place du Parc, 7000 Mons, Belgium

## Slide 2
CO2 emissions
Chart: 
| Energy industries | Transport | Manufacturing Industries and Construction | Residential | Industrial Processes and Product Use | Commercial | Agriculture | Other
Other Fuel Combustion Land-Use Change and Forestry Industrial Processes Building Manufacturing/Construction Transportation Electricity/Heat | 2.3413 | 3.1422 | 4.6231 | 7.5962 | 17.2809 | 20.7979 | 44.2184
Electricity and heat
Transport
Manufacturing and construction
Buildings
Industrial processes
Land use change and forestry
Other
CO2 capture
Absorption
Adsorption
Membrane technology
Micro-algae
Cryogenics
CO2 Utilisation or Storage
etc…
Food processing
Chemicals
Fuel and biofuel
Conventional amine-based absorption-regeneration process
Geological storage
Total worldwide CO2 emissions (1990 – 2021) [1]
CO2 emissions by sector in the world (2021) [1]
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
 | 23.0604 | 23.2174 | 23.168 | 23.3112 | 23.4576 | 24.0864 | 24.4347 | 25.5468 | 25.1547 | 25.2276 | 25.9239 | 26.0108 | 26.7312 | 27.6025 | 29.073 | 29.9082 | 31.1394 | 31.8259 | 32.0313 | 31.9533 | 33.522 | 33.4296 | 33.8162 | 34.4695 | 34.8564 | 34.6863 | 35.3833 | 35.8777 | 36.8653 | 37.0463 | 34.8196 | 36.6934
36.7 Gt in 2021
Polymers
etc…
Use of catalysts
Selection of catalysts for the regeneration step in an amine-based absorption-regeneration CO2 capture process
Célia PASTE (celia.paste@umons.ac.be), Lionel DUBOIS and Diane THOMAS Chemical and Biochemical Process Engineering Unit, Faculty of Engineering, University of Mons, 20 Place du Parc, 7000 Mons, Belgium
Image from: [3]
Context of the study

## Slide 3
7 steps of catalytic desorption of CO2 from MEA
MoO3
V2O5
Cr2O3
TiO2
WO3
ZnO
ZrO2
Nb2O5
Ag2O
NiO
CuO
MnO2
γ-Al2O3
H-ZSM5
H-Y
H-Mordenite
H-Beta
SAPO-34
MCM-41
SBA-15
KIT-6
ZEOLITES
MESOPOROUS SILICAS
METAL OXIDES
NATURAL CLAYS
Attapulgite
Montmorillonite
Enhance CO2 desorption
23 catalysts to study
Chart: Time (min)
Without catalyst (5M MEA)
With catalyst (5M MEA)
A1
A2
Increase in the amount of CO2 desorbed (%) = 100
Increase in CO2 desorption kinetics
4 main categories
Which catalyst to use ?
Based on [4]
Carbamate formation
Proton acceptance from a Brønsted acid site
Chemisorption of MEACOOH on the catalyst surface (Oxygen binds to a Lewis acid site)
Proton transfer from Oxygen to Nitrogen
Nitrogen-Oxygen bond stretch
N-C bond breakage due to a 2nd Lewis acid site on the Nitrogen
Separation and desorption of CO2
4 criteria
2. Performances based on literature data
3. Economic
criterion
4. Safety
criterion
1. Physicochemical properties
similar operating conditions
Selection of catalysts for
amine-based solvent regeneration
Cyclic catalytic mechanism of CO2 desorption
for a same amount of energy supplied to the system

## Slide 4
1. Physicochemical properties
2. Performances at lab scale from literature
Chart: 
| TiO2
HZSM5 | 1
MCM-41 | 58.512
KIT-6 | 209.76
SBA-15 | 340
Montmorillonite | 1.051
Attapulgite | 195.6
Chart: Price catalyst/Price H-ZSM5 (-)
| TiO2
TiO2 | 0.47553
Al2O3 | 0.62194
HZSM5 | 1
Cr2O3 | 1.2753
ZrO2 | 1.4931
MnO2 | 2.0376
V2O5 | 2.42
ZnO | 2.7588
MoO3 | 3.388
NiO | 4.3318
CuO | 5.0457
WO3 | 6.7034
3. Economic criterion
4. Safety criterion
H330: Fatal if inhaled (V2O5)
H350: May cause cancer (V2O5)
H350i: May cause cancer by inhalation (NiO)
H362: May cause harm to breast-fed children (V2O5)
H372: Cause damage to organs to prolonged or repeated exposure (V2O5 and NiO)
H410: Very toxic to aquatic life with long lasting effects (CuO and ZnO)
Grain of catalyst
Brønsted Acid Site (BAS) (proton donors)
Lewis Acid Site (LAS) (lone pair of electrons acceptors)
Chemical properties
The catalyst must have a maximum of number BAS and LAS
Physical properties
A large mesoporous surface area is necessary to allow chemical species to reach the catalytic sites.
TiO2
γ-Al2O3
H-ZSM5
Cr2O3
ZrO2
MnO2
V2O5
ZnO
MoO3
NiO
CuO
WO3
Nb2O5
Ag2O
Reference: H-ZSM5
1
1
1
H-Y
H-Beta
SAPO-34
H-Mordenite
MCM-41
H-ZSM5
KIT-6
SBA-15
Atta
-pulgite
Montmo
-rillonite
Hazard statements very striking
Catalysts V2O5 NiO, CuO and ZnO have been eliminated from the selection process
Reference: H-ZSM5
Metal oxides
Difficult to compare catalysts between studies because of different operating conditions:
Desorption temperature
Compare the catalysts against a reference catalyst widely used in studies: H-ZSM5 (zeolite).
NB: KIT-6, attapulgite and montmorillonite could not be compared with H-ZSM5 (data not available)
Desorption time
Solvent
Catalyst concentration
Metal oxides
Zeolites
Mesoporous silicas
Natural clays
Selected catalysts
MoO3
Cr2O3
ZrO2
Nb2O5
γ-Al2O3
H-ZSM5
H-Mordenite
H-Beta
ZEOLITES
METAL OXIDES
Zeolites, mesoporous silicas and natural clays
8 selected catalysts
5 of 13 selected
3 of 5 selected
Selection of catalysts for amine-based solvent regeneration: 4 criteria

## Slide 5
Micro-pilot experiments
References and Acknowlegdments
[1] Climate Watch, Historical GHG Emissions [Internet]. [cited 2024 Sep 16].
Available from: https://www.climatewatchdata.org/ghg-emissions?end_year=2021&start_year=1990
[2] T. Nakagaki, I. Tanaka, Y. Furukawa, H. Sato, and Y. Yamanaka, “Experimental evaluation of effect of oxidative degradation of aqueous monoethanolamine on heat of CO2 absorption, vapor liquid equilibrium and CO2 absorption rate,” in Energy Procedia, Elsevier Ltd, 2014, pp. 2384–2393. doi: 10.1016/j.egypro.2014.11.260.
[3] L. Xing, Z. Chen, G. Zhan, Z. Huang, L. Wang, and J. Li, “Efficient CO2 Desorption Catalysts: from Material Design to Kinetics Analysis and Application Evaluation,” Engineering, Sep. 2024, doi: 10.1016/j.eng.2024.08.024.
[4] A. H. Bhatti, M. Waris, W. W. Kazmi, K. H. Kang, and U. H. Bhatti, “Acid-treated activated carbon as simple and inexpensive catalyst to accelerate CO2 desorption from aqueous amine solution,” Carbon Capture Science and Technology, vol. 8, Sep. 2023, doi: 10.1016/j.ccst.2023.100131.
[5] U. H. Bhatti, D. Sivanesan, D. H. Lim, S. C. Nam, S. Park, and I. H. Baek, “Metal oxide catalyst-aided solvent regeneration: A promising method to economize post-combustion CO2 capture process,” J Taiwan Inst Chem Eng, vol. 93, pp. 150–157, Dec. 2018, doi: 10.1016/j.jtice.2018.05.029.
[6] U. Hassan Bhatti et al., “Effects of Transition Metal Oxide Catalysts on MEA Solvent Regeneration for Post-combustion Carbon Capture Process,” ACS Sustain Chem Eng, 2017, doi: 10.1021/acssuschemeng.7b00604.
[7] U. H. Bhatti, S. Nam, S. Park, and I. H. Baek, “Performance and Mechanism of Metal Oxide Catalyst-Aided Amine Solvent Regeneration,” ACS Sustain Chem Eng, vol. 6, no. 9, pp. 12079–12087, Sep. 2018, doi: 10.1021/acssuschemeng.8b02422.
Bibliographic review
  Understanding the role of the catalyst
  Selection of catalysts
Done
2. Regeneration experiments
  Lab-scale tests with powder
  Shaping of catalysts
  Micro-pilot tests with pellets
In progress…
3. Simulations
  Validation of micro-pilot tests
  Larger-scale simulation of the most promising case
To be done
This work was supported by the Fonds de la Recherche Scientifique-FNRS under Grant T.0218.23 (research project ATLANTIS)
Desorption column with catalyst
Micro-pilot simulation flowsheet
Project overview
Lab-scale experiments
1. CO2 loading of amine-based solvent
2. Solvent regeneration with gas and liquid analyses
3. Comparison of catalysts
Conclusion and prospects